## Slide 1: SmartNet: A European research project to study TSO-DSO coordination for ancillary services provision from distribution networks
Gianluigi Migliavacca (RSE)

## Slide 2: Agenda
General project overview
Five coordination schemes
Ancillary services market set-up
Bidding strategies
ICT analysis process and results
Aggregation algorithms
Three physical pilots

## Slide 3: The SmartNet project
architectures for optimized interaction between TSOs and DSOs in managing the purchase of ancillary services from subjects located in distribution.
three national cases (Italy, Denmark, Spain);
ad hoc simulation platform (physical network, market and ICT)
CBA to assess which TSO-DSO coordination scheme is optimal for the three countries.
use of full replica lab to test performance of real controller devices.
three physical pilots to demonstrate capability to monitoring and control distribution by the TSO and flexibility services that can be offered by distribution (thermal inertia of indoor swimming pools, distributed storage of radio-base stations).
http://SmartNet-Project.eu

## Slide 4: Overall project layout

## Slide 5: Comparison of the national cases in a simulation environment and laboratory testing
Lab implementation of the simulation environment
Cost Benefit Analysis
Development of simulation software
Definition of the reference scenario
Simulation
2030
Analysis of TSO-DSO coordination schemes
Definition of flexible devices profiles
Country-specific aspects and regulation
Network planning and operation
ICT specification and planning
Physical layer
Aggregation and bidding
Market layer
database

## Slide 6: TSO-DSO coordination schemes
5 possible coordination schemes TSOs & DSOs for AS by distributed flexibility resources
Centralized AS market model
Local AS market model
Shared balancing responsibility model
Common TSO-DSO AS market model
Integrated flexibility market model

## Slide 7: Ancillary services market set-up
The market is a closed-gate auction. The clearing frequency is chosen close to real-time (e.g. 5 minutes).
The market uses a rolling optimization. The optimization window (or horizon) contains several time steps (e.g. 1 hour)
Output of the first time step is a firm decision. It contains the actual activation of flexible assets and has to be followed by the aggregators/owners.
Output of the next time steps are advisory decisions. They will assist the aggregators and the TSO to anticipate the availability of flexibility in the upcoming time steps.

## Slide 8: Arbitraging between markets
A – The aggregator will be better off pricing his flexibility in wholesale intraday market and not wait for SmartNet Market . He will buy back his production on intraday, and will be meant to not produce in real-time. However, he can always bid for up-regulation.
B - The aggregator can profit from lower cost buying back his production from SmartNet Market compared to intraday. This is the most likely situation
C - The Aggregator can buy energy from SmartNet market at down regulation price but do nothing, hence settling the excess energy at a higher balancing settlement price, for which he can make a risk-less arbitrage. Such kind of offers are likely to be out-of-merit order and, in any case, market mechanism and grid codes should rule them out.
Markets tend to converge to balancing settlement prices

## Slide 9: ICT analysis process and results

## Slide 10: The aggregation algorithms
The aggregator acts on behalf of the service providers on the electricity market:
determining the price and the quantity of individual bids (per node),
performing aggregation (before bidding on the market)
Performing disaggregation (after getting market clearing results)
PHYSICAL (bottom-up): horizontal summation of power for the individual devices: the aggregator knows all of the parameters of each individual device and also its real time status. It becomes difficult to implement when many heterogeneous energy resources are included
TRACES: the aggregation is represented by all the possible combinations of feasible profiles of all the devices.
HYBRID: uses a single, or a limited number of virtual devices in order to represent the entire population of aggregated devices. Such practice reduces the number of individual devices and avoids exhaustive bid parametrization. Should the number of clusters equal the number of individual devices, the hybrid approach becomes the physical, bottom-up, approach.

## Slide 11
Pilot A: Distribution monitoring and control

## Slide 12
Pilot B: Ancillary services from indoor swimming pools

## Slide 13
Pilot C: Ancillary services from radio-base stations

## Slide 15
Gianluigi Migliavacca
Contact Information
Affiliation: RSE S.p.A.
Phone: +39 02 3992 5489
Email: gianluigi.migliavacca@rse-web.it