## Slide 1: TSO-DSO Coordination Schemes for Accommodating Ancillary Services from Distribution Networks
Helena Gerard, Enrique Rivero Puente, Daan Six
12th IEEE PES PowerTech Conference
Special session SmartNet | Manchester |19.06.2017

## Slide 2: Agenda
TSO-DSO coordination schemes: scope and definitions
Characteristics of 5 TSO-DSO coordination schemes for flexibility- based services
Conclusions

## Slide 3: Agenda
TSO-DSO coordination schemes: scope and definitions
Characteristics of 5 TSO-DSO coordination schemes for flexibility- based services
Conclusions

## Slide 4: TSO-DSO coordination schemes: scope and definitions
Objective: analyze TSO-DSO coordination schemes (CSs) for the provision of flexibility-based system services by distributed resources (DG, DSM, …)
Analyse each CS, focusing on:
  envisioned set of roles and responsibilities,
  potential market architectures, and
  relevant information exchanges
Impact on TSO grid operation, DSO grid operation, the role of other market participants and the related market design  national regulatory frameworks and EU context
Notes: Within SmartNet an use case is defined as “the provision of a service, within the framework of a certain coordination scheme, from one actor to another actor”.
Analysis of internal and external aspects of coordination schemes, taking into account the different phases of procurement, and activation of flexibility-based services.
Each coordination scheme is characterized by a set of roles, taken up by TSOs, DSOs and other market players, and a market design, in line with these roles. The distinction between roles is essential as the increased need for coordination between network operators should not create any confusion in allocating respective roles and responsibilities [5].
A role is defined as an intended behavior of a specific market party which is unique and cannot be shared. Each role has certain responsibilities inherent to the role. A role defines how one market party interacts with another market party during a certain transaction [22].

## Slide 5: Agenda
TSO-DSO coordination schemes: scope and definitions
Characteristics of 5 TSO-DSO coordination schemes for flexibility- based services
Conclusions

## Slide 6: Five possible TSO-DSO coordination schemes: 1) Centralized AS market model
1 common ancillary services market managed by TSO
Separate DSO process for checking distribution constraints (e.g. prequalification)
Notes: Characteristics
Market design
There is one common market for ancillary services, operated by the TSO, for both resources connected at transmission and distribution level. There is no separate local market.
TSO role
The TSO is responsible for the operation of its own market for ancillary services. DSO constraints are not explicitly taken into account. A separate process (system prequalification) could be installed to guarantee that the activation of resources from the distribution grid by the TSO does not cause additional constraints at the DSO-grid (e.g. congestion).
DSO role
The DSO is not involved in the procurement and activation process of AS by the TSO, except in the case that a process of system prequalification might be installed. The DSO is not procuring local flexibilities in real-time or near to real-time.
The general process of prequalification could be divided in two separate processes: technical prequalification and system prequalification). A technical prequalification validates the technical requirements of a unit that wants to participate to the AS market. System prequalification is defined as an up-front process where the DSO validates the participation of DER to the flexibility market, under the condition that it does not violate local grid constraints. More detailed information related to system prequalification can be found in section 4.3.

## Slide 7: Five possible TSO-DSO coordination schemes: 2) Local AS market model
Separate local market managed by DSO for local issues
Transfer remaining flexibility to TSO ancillary services market level
Notes: Characteristics
Market design:
There is a separate local market managed by the DSO. Resources from the DSO grid can only be offered to the TSO via the DSO/local market and after the DSO has selected resources needed to solve local congestion. The DSO aggregates and transfers bids to the AS market, operated by the TSO. The DSO assures that only bids respecting the DSO grid constraints can take part in the AS market.
Role of TSO:
The TSO is responsible for the operation of its own market for ancillary services, where both resources from the transmission grid and resources from the distribution grid (after aggregation by the DSO) can take part.
Role of the DSO:
The DSO is the operator of a local market for flexibility. The DSO clears the market, select the necessary bids for local use, and aggregates and transfers the remaining bids to the TSO-market.

## Slide 8: Five possible TSO-DSO coordination schemes: 3) Shared balancing responsibility model
Ancillary services market for transmission grid-connected resources managed by TSO
Local market for distribution grid-connected resources
Agreed pre-defined TSO-DSO scheduled profile
Notes: Characteristics
Market design:
There is an AS market for resources connected at TSO-grid, managed by the TSO. There is a separate local market for resources connected at the DSO-grid, managed by the DSO. Resources from the DSO grid cannot be offered to the TSO-grid. DSO constraints are integrated in the market clearing process.
Role of TSO:
The TSO is the operator of the AS market, limited to resources connected at the transmission level. The TSO is responsible for the balancing of the transmission grid.
Role of the DSO:
The DSO is the operator of a local market. The DSO contracts local flexibility for both local congestion management and balancing of the DSO-grid. The DSO is responsible for the balancing of the DSO-grid, i.e. respecting the pre-defined schedule.

## Slide 9: Five possible TSO-DSO coordination schemes: 4) Common TSO-DSO AS market model
Common flexibility market managed jointly by TSO & DSO
Variants:
  One optimization with all grid constraints
  Two optimizations: distribution & transmission constraints
Notes: Characteristics
Market design:
There is a common market for flexibilities for both TSO and DSO with both resources connected at transmission level and connected at distribution level. TSO and DSO are both responsible for the organization and operation of the market. DSO constraints are integrated in the market clearing process. Two alternatives are considered: (1) all constraints are integrated in one only optimization process that encompasses both TSO and DSO grid constraints (centralized variant), (2) a separate local DSO market for local grid constraints runs first (without commitment to the market participants) and communicates with an AS market operated by a TSO with distribution and transmission grid connected resources. The outcome of the second market communicates back to the first market to find the optimal solution to be communicated to the market participants (decentralized variant).
Role of TSO:
The TSO and DSOs are jointly responsible for the market operation of the common TSO-DSO market (centralized variant) while they are jointly responsible for the final outcome of the two separate market runs (decentralized variant). The TSO is contracting AS services from both transmission and distribution . In practice, in the centralized variant, the joint responsibility could be organized by allocating the responsibility to a third party, under guidance of both TSOs and DSOs.
Role of the DSO:
The TSO and DSOs are jointly responsible for the market operation of the common TSO-DSO market (centralized variant) while they are jointly responsible for the final outcome of the two separate market runs (decentralized variant). The DSO envisions AS services from distribution grid in cooperation and interaction with the TSO.

## Slide 10: Five possible TSO-DSO coordination schemes: 5) Integrated flexibility market model
Common flexibility market managed by an independent / neutral market operator
No priority for TSO, DSO or commercial market player
Notes: Characteristics
Market design:
The common market for flexibilities is organized according to a number of discrete auctions and is operated by an independent/neutral market operator. There is no priority for TSO, DSO or CMP. Resources are allocated to the party with the highest willingness to pay. There is no separate local market. DSO constraints are integrated in the market clearing process.
Role of TSO:
TSOs are contracting AS services in a common market. TSOs can sell previously contracted DER to the other market participants.
Role of the DSO:
DSOs are contracting flexibilities for local purposes in a common market. DSOs can sell previously contracted DER to the other market participants.

## Slide 11: Five possible TSO-DSO coordination schemes: Benefits and attention points

## Slide 12: Five possible TSO-DSO coordination schemes: Benefits and attention points

## Slide 13: Five possible TSO-DSO coordination schemes: Benefits and attention points

## Slide 14: Agenda
TSO-DSO coordination schemes: scope and definitions
Characteristics of 5 TSO-DSO coordination schemes for flexibility- based services
Conclusions

## Slide 15: TSO-DSO coordination schemes: conclusions
Different possible TSO-DSO coordination schemes: each have their own benefits and risks
Different coordination schemes imply different roles, responsibilities, market design, regulation, grid operation, cost of implementation, …
Mathematical formulation and implementation ongoing
Public deliverable available:
http://smartnet-project.eu/wp-content/uploads/2016/12/D1.3_20161202_V1.0.pdf
If they want to go fast, system operators could go alone; if they want to go far, they should go together,
turning challenges into opportunities
Notes: Benefits
Risks
Scenario 1
(distribution constraints not considered)
- No additional cost
- Constraints might not be respected
Scenario 2
(DSO involved in system prequalification)
- Implementation costs might be low - DSO grid constraints are taken into account - Provides more information to the DSO (enhancing grid observability)
- Constraints might not be respected
- Need for accurate long-term forecasts of future grid load
- In order to secure the grid, safety margins taken by the DSO might be very conservative
Scenario 3
(DSO also involved after market clearing)
- DSO grid constraints are always respected - Provides more information to the DSO (enhancing grid observability)
- Mathematically not difficult to implement
- Heavy operational process (manual and iterative)
- Deadline of finishing the market clearing process might be endangered by this process - Could create uncertainty in the market as it is unclear on which base DSOs might block activations - Issues with transparency
Scenario 4
(Constraints integrated in market clearing)
- DSO grid constraints are always respected - Provides more information to the DSO (enhancing grid observability)
- Operational process is relatively light
- No issues related to ‘neutrality’ of the DSO
- Heavy mathematical process to integrate all constraints in the clearing
Need for sharing data between DSO and market operator (discussions on security and privacy of data)

## Slide 17
Daan Six
Contact Information
Affiliation: VITO / EnergyVille
Phone: +32 14 33 58 47
Email: daan.six@vito.be / daan.six@energyville.be