## Slide 1: Advanced market schemes for allowing ancillary services from distribution networks
Guillaume Leclercq
Senior Consultant
N-SIDE

## Slide 2: Market architecture for TSO-DSO coordination schemes
Defining a new ancillary service (AS) market for TSO-DSO coordination schemes
What is required?
Ensure a safe AS procurement at the lowest cost for system operators
Extract flexibility of distributed energy resources (DERs) in an efficient way
Allow a level playing field for competition between different sources of flexibility
Valorize flexibility at its real value for the power system
What has to be avoided?
Discouraging participation of DERs by not taking into account their constraints
Creating congestion and/or voltage problem by activation at a wrong location
Making myopic real-time decisions that compromise an efficient balancing management for future time steps
Notes: Having defined a bunch of possible coordination schemes between TSO and DSO to procure AS and local services, it is this necessary to specify the market desgin and algorithm for each of them.
Independently of the coordination schemes, we (SmartNet project) also aim at providing advanced market schemes, to answer a few requirements:

## Slide 3: Key market design ingredients
Bidding Dimension
Clearing
Dimension
Network
Dimension
Pricing
Dimension
How market actors can bid ? What market products are proposed?
What are the market clearing frequency, time step and horizon ?
How network constraints are taken into account in the market clearing ?
What price is paid to the activated bids ?
Timing Dimension
What are the objectives of the market clearing ?
Notes: We identify 5 key market design ingredients

## Slide 4: Key market design ingredients
Bidding Dimension
Clearing
Dimension
Network
Dimension
Pricing
Dimension
How market actors can bid ? What market products are proposed?
What are the market clearing frequency, time step and horizon ?
How network constraints are taken into account in the market clearing ?
What price is paid to the activated bids ?
Timing Dimension
What are the objectives of the market clearing ?

## Slide 5: Market Design: Timing
The market is a closed-gate auction. The clearing frequency is chosen close to real-time (e.g. 5 minutes).
The market uses a rolling optimization. The optimization window (or horizon) contains several time steps (e.g. 1 hour)
Output of the first time step is a firm decision. It contains the actual activation of flexible assets and has to be followed by the aggregators/owners.
Output of the next time steps are advisory decisions. They will assist the aggregators and the TSO to anticipate the availability of flexibility in the upcoming time steps.

## Slide 6: Key market design ingredients
Bidding Dimension
Clearing
Dimension
Network
Dimension
Pricing
Dimension
How market actors can bid ? What market products are proposed?
What are the the market clearing frequency, time step and horizon ?
How network constraints are taken in the market clearing ?
What price is paid to the activated bids ?
Timing Dimension
What are the objectives of the market clearing ?

## Slide 7: Market Design: Products
Market allows various bid format, accompanied by temporal and logical constraints:
Accept-All-Time-Steps-or-None:  Profile tracking
Ramping:  Turbines
Max. number of activations:  Avoiding wear & tear
Max. duration of activation:  Air conditioning
Min. duration of activation:  Plant efficiency
Min. delay between activations:  Avoiding wear & tear; cool-down and warm-up
Integral:  Electric storage
Implication:  Series factory lines
Exclusive Choice:  Parallel factory lines
Deferability:  Wet appliances
Logical constraints (Inter-bid)
Temporal constraints (Intra-bid)
Notes: We propose a catalogue of market products, from:
simple bids (single quantity-price pair over one time step)
Simple bids with multiple pairs (quantity-prices)
Non-curtailable bids
Bids covering multiple time steps of the market time horizon  for those, we can define different inter-temporal constraints
Constraints between bids (exclusive, implication)
All those products must not necessarily be used by a specific instance of market design but it is worth to test which are wortwhile and also wich ones generate computational burden on the market clearing algorithm: typically those involving integer variables

## Slide 8: Key market design ingredients
Bidding Dimension
Clearing
Dimension
Network
Dimension
Pricing
Dimension
How market actors can bid ? What market products are proposed?
What are the the market clearing frequency, time step and horizon ?
How network constraints are taken into account in the market clearing ?
What price is paid to the activated bids ?
Timing Dimension
What are the objectives of the market clearing ?

## Slide 9: Market Design: Network
1 Photo source: Technical University of Munich (http://ens.ei.tum.de)
Transmission grid
MV distribution grid
LP
AC (NLP)
Copper plate
SOCP
LP
AC (NLP)
Copper plate
+ Accuracy
+ Numerical Complexity
+ Accuracy
+ Numerical Complexity
1
SOCP Problem (Convex)
Notes: Network models to be considered to avoid creating current congestions or voltages problem.
Best is to have full AC models, but non-linear  not likely to be tractable in the market clearing algo  need to simplify:
Linear is ok for meshed transmission grid (voltage problems are supposed to be solved independently)
SOCP (convex) is the chosen approach for MV distribution grid, to be able to model reactive power and voltage implicaitons (more realistic and less decoupled than for distribution grid)
Market clearing algorithm will thus be a MISOCP problem

## Slide 10: Key market design ingredients
Bidding Dimension
Clearing
Dimension
Network
Dimension
Pricing
Dimension
How market actors can bid ? What market products are proposed?
What are the the market clearing frequency, time step and horizon ?
How network constraints are taken in the market clearing ?
What price is paid to the activated bids ?
Timing Dimension
What are the objectives of the market clearing ?

## Slide 11: Market Design: Objective
Maximization of Welfare versus Minimization of Activation Costs
Should we only activate what is necessary, or favor extra welfare by allowing additional exchanges?

## Slide 12: Key market design ingredients
Bidding Dimension
Clearing
Dimension
Network
Dimension
Pricing
Dimension
How market actors can bid ? What market products are proposed?
What are the the market clearing frequency, time step and horizon ?
How network constraints are taken in the market clearing ?
What price is paid to the activated bids ?
Timing Dimension
What are the objectives of the market clearing ?

## Slide 13: Market Design: Pricing
Options to define the price received by activated bids:
Pay as Bid: The same price that was provided during the bidding.
Pros: Simplifies the pricing mechanism. Cons: It does not encourage to bid at real marginal cost of flexibility. Reduces welfare. Reduces transparency.
B. Zonal Marginal Price: One price per region/zone/area.
Pros: Projects value of flexibility at each zone. Less complex than nodal pricing. Cons: How to define the zone sizes? One price for each distribution network? Does not reflect real local needs in pricing
C. Locational Marginal Price: A single price at each node of the transmission and distribution(s) networks.
Pros: Projects real value of flexibility at each node. Cons: Complex pricing mechanism. Intuitiveness.
Locational Marginal Pricing as the preferred option

## Slide 14: Summary
Defining a new ancillary service (AS) market for TSO-DSO coordination schemes:
What is required?
AS procurement at the lowest cost Mathematical optimization
Extract flexibility of DERs Open for aggregated/non-aggregated bids
Allow a level playing field for competition Variety of market products
Valorize flexibility at its real value Nodal pricing
What has to be avoided?
Not taking into account DERs' constraints Complex products
Creating congestion and voltage problem Integrated detailed network model
Making myopic decisions Rolling optimization

## Slide 15: Decentralized vs Centralized Market architecture
TSO-DSO Coordination Schemes
Adaptations needed for decentralized architectures
Centralized market architecture
Decentralized architecture
HV
MV
G
L
G
L
LV
G
L
LV
Distribution grid 1
Distribution grid 2
HV
MV
G
L
G
L
LV
G
L
LV
Distribution grid 1
Distribution grid 2
bid
bid
Aggregation of bids from local market by DSO while respecting distribution grid constraints, to submit on global markets: Local AS market, Common TSO-DSO AS market (decentralized) OR no interaction between markets if exchange profile agreed in advance (Shared balancing responsibility model)
Timing: Synchronization between markets is needed
Possibility to have different market settings (products definition) between central and local markets.
Centralized
Decentralized
Centralized AS market
Common TSO-DSO AS market (centralized)
Integrated flexibility market
Local AS market
Common TSO-DSO AS market (decentralized)
Shared balancing responsibility model

## Slide 16: Challenges and next steps
Your feedback is welcome : preliminary report on market design and algorithm (Deliverable D2.4) available on SmartNet website
http://smartnet-project.eu/
Next steps:
  Continue implementation of the different market clearing algorithms for the different TSO-DSO coordination schemes
  Test, Scale and Report on speed vs accuracy tradeoff
  Investigate efficients methods for scalability (decomposition methods)
Challenges
  Tractability issues: solving a MISOCP (market clearing) in a few minutes, while considering: transmission and distribution grid constraints (SOCP model)), a receding time horizon and complex market products (integer variables)
  Data availability: e.g. prediction of injection/offtake at network nodes, scheduled TSO-DSO exchange profile.

## Slide 18: Market Design: Objective
Objective: Maximization of Social Welfare & Avoiding Unnecessary Activations
Adaptation of prices for bids with wrong direction
Summation over bids with positive/negative values for q and p

## Slide 19: Market Design: Pricing
Calculating Distributed Locational Marginal Prices (DLMP) in which the clearing algorithm assigns individual prices for each node of the grid.
A difference between DLMPs is a result of two phenomena in the lines:
  Energy losses (as a result of non-zero impedance)
  Network constraints (line capacity limits and congestions)
3
2
1
Load
Load
Generator
+40 MW
-20 MW
-20 MW
Loss = 0
No Congestion
Loss = 0
No Congestion
Price: +30 €/MWh
Price:
-30 €/MWh
Price: -30 €/MWh
3
2
1
Load
Load
Generator
+44 MW
-20 MW
-20 MW
Loss = 2 MW
No Congestion
Loss = 2 MW
No Congestion
Price: +30.5 €/MWh
Price:
-31 €/MWh
Price: -32 €/MWh
3
2
1
Load
Load
Generator
+46 MW
-20 MW
-20 MW
Loss = 2 MW
No Congestion
Loss = 2 MW
Limit: 15 MW
Price: +31 €/MWh
Price:
-32 €/MWh
Price: -35 €/MWh
4
No loss, no congestion
Losses, but no congestion
Both losses and congestions