## Slide 1: The way forward
Gianluigi Migliavacca (RSE)
Final public workshop| 16. 05.2019

## Slide 2: Agenda
The juice
Some conclusive remarks
What will remain after the light is turned off
Thanks!

## Slide 3: Coordination Schemes comparison: the juice (1/2)
<number>
Technical reasons advise to continue centralizing balancing responsibility to TSOs.
Local services and, in particular, congestion management could be shared, instead (coherently with what stated in the EC package: Clean Energy for All Europeans).
Shallow or deep distribution constraints management?
  Traditional TSO-centric schemes could stay optimal if distribution networks don’t show significant congestion not unlikely in near-future scenarios, since distribution grid planning was (and still is) affected by the fit-and-forget reinforcements policy. Abandoning the fit-and-forget policy is presently disfavoured by the current regulation, remunerating DSO for investments in grid elements (CAPEX) rather than in intelligence (OPEX).
  More advanced centralized schemes incorporating distribution constraints show higher economic performances but their performance could be undermined by big forecasting errors: it is important that the gate closure is shifted as much as possible toward real time, market clearing frequency is increased and forecasting techniques are improved.

## Slide 4: Coordination Schemes comparison: the juice (2/2)
Local or centralized schemes
  Decentralized schemes are usually less efficient than centralized ones because of the two-step optimization process and of some consequent undue rigidities (e.g. imposing flow at the TSO-DSO interface in CS-C).
  Scarcity of liquidity and potential impact of local market power (not investigated in SmartNet), along with extra constraints introduced to avoid counteracting actions between local congestion market and balancing market (e.g. increasing system imbalance while solving local congestion) furthermore negatively affect economic efficiency of decentralized schemes.
  Local congestion markets should have a “reasonable” size and guarantee a sufficient number of actors are in competition in order to prevent scarcity of liquidity and exercise of local market power. Small DSOs could need to pool-up.
Market products
  Ensuring level playing field in the participation of distributed resources (especially industrial loads) to the tertiary market means to be able to incorporate into the market new products taking into account some peculiarities of such resources

## Slide 5: Some conclusive remarks
Provided:
  the regulation helps to abandon the fit-and-forget (oversizing) planning policy in Distribution,
  forecasting errors are coped with,
CS-D (integrated TSO-DSO scheme) could show its superiority over CS-A. However, due to complexity reasons, the “depth” cannot be pushed till single LV nodes.
For them, a methodology foreseeing a real time estimation of the Capability Curve (see experience of Pilot A) could be profitably employed.
However, providing observability of the distribution grids implies new important investments by the system. As during the first years the entity of such investments could be higher than the advantages, proper regulatory incentivisation could help considerably.
Applying strict time specification (4 seconds for control) to machines that were not put into service for this can generate problems of slow response (Pilot A). ICT readiness and response should also be tested (Pilot B). In case, it could be important to find a role for the new flexibility taking into account inherent limitations. Taking this in mind could call to restructure current reserves procurement modalities.

## Slide 6: What will remain after the light is turned off
A comprehensive SW platform already run on three national cases, but which could be used to study further cases whenever of interest for the European stakeholders.
A new methodology to compare CS on the basis of an objective CBA
Very detailed benchmark scenarios at 2030 for Italy, Denmark and Spain
Three national pilots which could be seen by Regulators as a starting point for national Sandboxes.
An in-depth analysis of the simulation results, which brought to the formulation of a set of regulatory guidelines as a final view of the project targeted to Regulators and Institutions: deliverable D6.3 is in public consultation on the SmartNet web and will wait for Stakeholders feedbacks (deadline in one month from now).
All main SmartNet achievements are summarized in a booklet available on the SmartNet web site.

## Slide 7: Thanks!
I would like to say thank you to all SmartNet partner for the excellent team work done in 3.5 years of project activities
Special thanks to:
  The RSE Team: M. Rossi, G. Viganò, D. Siface
  The WP Leaders: H. Gerard, M. Dzamarija, S. Horsmanheimo, M. Rossi, C. Madina, I, Kockar, D. Bernardo
  The Pilot Leaders: L. Ortolano, H. Madsen, M. Pardo
  The simulation runs management by N-SIDE: G. Leclercq, P. Sels, O. Devolder
  The management of communication, Internet site, booklet…: D. Bernardo, C. Canestrini

## Slide 9
Gianluigi Migliavacca
Contact Information
Affiliation: RSE S.p.A.
Phone: +39 02 3992 5489
Email: gianluigi.migliavacca@rse-web.it